## Slide 1: Battery Degradation Early Warning

## Slide 2: A leakage-resistant research design using capacity, EIS and operating history
Current stage: protocol + synthetic contract implementation No trained KIT model; no prediction result claimed
Lu Zhang — independent public-data research project

## Slide 3: INTRODUCTION — The operational problem
Today's check-up What we want to know Human decision capacity + EIS -> future degradation risk -> monitor / inspect / service history + context conditional remaining life with evidence
Capacity loss and impedance growth affect useful battery life.
A current measurement describes now; maintenance needs evidence about what may happen next.
The research unit is a physical battery cell—not a spectrum or frequency row.
Scope: degradation and capacity-defined end of life.
Not in scope: thermal runaway, fire or every sudden field failure.

## Slide 4: PURPOSE — Four research questions
Will the cell degrade rapidly over the next registered horizon?
Will it cross a declared capacity threshold soon?
Will it begin to diverge from cells under the same condition?
How much useful exposure remains if the declared use condition continues?
Main incremental-value question:
capacity history + use/context (B) versus capacity history + use/context + current EIS (D-core)
D-core versus B isolates what EIS adds.

## Slide 5: DATA DESCRIPTION — Origin and hierarchy
KIT version 2 result data, CC BY 4.0
228 physical cells = 76 operating conditions x 3 replicate cells -> repeated diagnostic check-ups -> capacity + pulse + EIS contexts -> one EIS spectrum -> 29 frequency rows (pre-audit observation)
Level | Meaning | Independent sample?
Cell | One physical 18650 battery | Yes
Condition | Shared ageing parameters for 3 cells | Primary split group
Check-up | Repeated diagnostic timepoint | No—same cell repeated
Spectrum | EIS at one SoC/temperature context | No
Frequency row | One complex-impedance point | No

## Slide 6: DATA DESCRIPTION — Three ageing modes and measurements
Mode | Between check-ups | Main lifetime coordinate
Calendar | Rest near target voltage/SoC | Days
Cyclic | Controlled repeated charge/discharge | Equivalent full cycles
Profile | Dynamic WLTP-derived demand + recharge | EFC; traceable distance secondary

## Slide 7
Measurement | What it contributes
Capacity/EOC | Q0, current capacity, history and future outcomes
EIS | Complex impedance spectrum at 10/30/50/70/90% SoC, RT and OT
Pulse | Optional resistance/relaxation evidence after audit
Temperature/context | Mode, temperature, voltage/SoC window, rates/profile

## Slide 8
Common check-ups make capacity and impedance more comparable across conditions.

## Slide 9: PROCEDURE — One prospective experiment from start to finish
1. audit source + lineage 2. choose prediction check-up t 3. build features from measurements completed through t 4. build outcome from strictly later check-ups (label side only) 5. assign whole conditions to development or protected evaluation 6. fit preprocessing, variable selection and model inside development folds 7. calibrate and compare A / B / C / D-core / D-full 8. freeze winner + policy -> authorize one protected test 9. produce evidence packet -> human-reviewed action
The scientific experiment is prospective: what was knowable at check-up t predicts what happens after t. Future observations may construct labels after authorization, but never features or fit.

## Slide 10: EDA & PREPROCESSING — Understand first, then freeze the boundary
Planned EDA evidence | Scientific reason
Cell/condition/check-up inventory | Verify cohort and effective sample size
Capacity trajectories with 3 replicates | See degradation shape and peer spread
Nyquist/Bode examples | Check EIS orientation and quality
Frequency/context missingness heatmap | Freeze eligible channels
Event + censoring counts | Decide whether targets are feasible
Exposure distributions by mode | Avoid mixing days, EFC and distance

## Slide 11
audit source -> align check-ups -> freeze Q0 -> target-free snapshots -> metadata-only condition split -> past inputs | strictly future labels -> fold-local missingness/imputation/scaling -> censored follow-up retained
Status: planned EDA artifacts; preprocessing contracts partly implemented on synthetic data only.

## Slide 12: FEATURE ENGINEERING & VARIABLE SELECTION
View | Inputs | Role
A | Capacity history | Trajectory baseline
B | A + use/environment | Strong non-EIS baseline
C | EIS + use/environment | EIS-centric alternative
D-core | B + EIS | Primary incremental-EIS test
D-full | D-core + pulse/temp/quality | Auxiliary-diagnostic ablation

## Slide 13
Fold-local selection:
quality filter -> impute/scale -> constant/correlation screen -> optional supervised selection -> model
Report selection frequency and importance stability across outer folds.

## Slide 14: MODELING & MODEL SELECTION — Complexity must earn selection
Eligible model ladder
Binary warnings: prevalence/rule baseline -> elastic-net logistic -> constrained boosting -> one additional calibrated nonlinear candidate only if independent groups support it.
Conditional RUL: empirical survival reference -> regularized Cox/AFT -> tree survival only after censoring and implementation review.
How a winner earns selection in nested held-condition OOF
paired gain beyond the preregistered one-standard-error simplicity margin;
acceptable calibration, false alerts, misses and worst-mode behavior;
stability across conditions, folds and seeds;
justified interpretation and compute cost; and
for the scientific claim, robust D-core > B evidence.
No primary RUL regressor that discards censored cells. No initial deep model: 228 cells and 76 condition groups are the effective scale. An ensemble requires 3+ complete, diverse same-outcome OOF sets, inner-fold weights, stable calibration and meaningful paired gain; otherwise it is rejected.
Current rationale: NOT YET SELECTED — AWAITING REVIEWED DEVELOPMENT TRAINING

## Slide 15: TRAINING — Planned evidence, not a completed run
Training evidence | Current value
Audited cells/conditions/events/censoring | NOT YET RUN
Outer/inner condition-group folds | NOT YET RUN
Views, candidates and hyperparameter budget | Registered; not executed
Trial runtime/CPU/memory/heartbeat | NOT YET RUN
Convergence, warnings and failures | NOT YET RUN
Data/code/registry/split/model lineage | Awaiting hash-bound run

## Slide 16
The implemented CLI is a synthetic contract demo. It does not load KIT, fit a model or satisfy the later real-data monitored training-smoke gate. It executes synthetic Q0/SoH, the next-three-check-up threshold label and a provisional human-reviewed action; the broader contracts are unit-tested rather than run by this command.

## Slide 17: PREDICTION RESULTS — Development packet structure
Status: NOT YET RUN / NO KIT MODEL RESULT
Future held-condition OOF report:
per-mode, per-temperature and per-condition results first;
PR-AUC, recall/precision at frozen alert budget, misses and false alerts;
calibration and event-level warning lead time;
survival integrated Brier score, concordance, calibration and interval coverage;
paired feature-view deltas, especially D-core - B;
worst cases, false positives/negatives and abstentions;
action-policy utility and stability.
No fake ROC/PR curve, trajectory or headline metric is used as a placeholder.

## Slide 18: VALIDATION / TEST — Leakage-resistant and one shot
metadata-only condition split -> nested development OOF -> independent metric + model-rationale review -> freeze model/features/calibration/actions/report -> separate human authorization -> one protected held-condition evaluation
All three replicate cells of a condition remain together.
Random row/spectrum/check-up splits are prohibited.
Test labels cannot choose variables, thresholds, seeds or ensemble weights.
Final protected result status: NOT AUTHORIZED.

## Slide 19: ANALYSIS — What the score alone cannot tell us
mode / temperature / condition errors + calibration + false positives / false negatives + lead-time distribution + censoring sensitivity + feature stability + failure cases + decision utility
Key causal restraint: D-core > B is evidence of incremental predictive value under this protocol; it is not proof that an impedance feature is a degradation mechanism.
A valid negative conclusion is possible: EIS advantage not demonstrated.

## Slide 20: DECISION OUTPUT — Evidence before action
validated snapshot -> calibrated risk + conditional RUL -> deterministic policy -> evidence packet -> human review
Level | Meaning | Suggested human-reviewed response
Green | No registered trigger | Continue scheduled monitoring
Yellow | Moderate risk or questionable data | Retest / shorten interval
Orange | Persistent high degradation risk | Inspect, consider derating, plan service
Red | Confirmed capacity criterion/repeated evidence | Service or replacement review

## Slide 21
CLI demonstration now: synthetic Q0/SoH + next-three-check-up threshold label + provisional action requiring human review. Other history, rapid-label, censoring, peer, split and metric contracts have unit-test coverage but are not CLI demo outputs. Not implemented: audited KIT loader, trained model, calibrated thresholds, validated UI decision.

## Slide 22: CONCLUSION — Current evidence and next milestones
Can conclude now
prospective question, data hierarchy and leakage boundary are defined;
the CLI demonstrates synthetic Q0/SoH, a next-three-check-up threshold label and a provisional human-reviewed action;
broader history, rapid-label, censoring, peer, split and metric contracts have unit-test coverage;
D-core versus B is the registered EIS-value test.
Cannot conclude now
no reviewed KIT training or prediction result;
no EIS advantage, RUL accuracy, warning lead time or deployed action validity proven.
Evidence needed next
audited KIT cohort -> label/censoring prevalence review -> grouped leakage tests -> observable real-data training smoke -> independent authorization -> nested development OOF -> model rationale -> protected one-shot test